## Slide 1: Annual Update On Interfaces
Mick Posner Product Line Group Director
January 25, 2023

## Slide 2
Multi-Die System Motivations and Use Cases
Multi-Die Challenges
Die-to-Die standard options
Result of Synopsys user survey
Why UCIe is the standard of choice for multi-die systems

## Slide 3: Synopsys Enables System Innovation, Silicon to Software
Broadest System Design Coverage
Software:
Application security & quality testing,
Leader in Gartner’s Magic Quadrant
Systems:
Leader in HW/SW verification, virtual prototyping, VIP and models
Design:
Digital & custom AMS families Best QoR, highest productivity
Solutions:
Automotive, low power, multi-die, DTCO, memory, SLM, optics, photonic IC
Silicon:
Reference tools for process optimization, CAD, lithography & yield optimization
IP:
Broadest portfolio, silicon-proven #1 in interface, foundation & physical IP
Comprehensive World-Class Technology
PROCESS
FUNDAMENTALS
DEPLOYED
SYSTEM

## Slide 4: Increasing Functionality With More Transistors
The number of transistors in a dense IC doubles about every two years
has been driven by Moore’s Law
For the last 50 years
the semiconductor industry
Animation 1
Animation 2
Animation 3
Animation 4
Animation 5
Animation 6
Animation 7
Animation 8
Animation 9
Animation 10
Animation 11
Animation 12
250nm
90nm
45nm
3nm
7nm
32/28nm
1996
Intel Pentium Deschutes
7.5M
Transistors
2003
IBM PowerPC 970
58M
Transistors
2022
Apple A16 Bionic
15B
Transistors
2018
Apple A12 Bionic
6.9B
Transistors
2010
Intel Westmere-EX
2.6B
Transistors
2007
Intel XEON 5400
820M
Transistors
Silicon Cost per Yield mm2

## Slide 5: Laws of Semiconductor are Faltering
Dennard Scaling (1974, Robert Dennard)
  Power Density/mm2 stays constant with doubling of density
  Has been breaking down since late 2000s, limits frequency scaling and causes power density challenges
Moore’s Law
  Cost/mm2 has been increasing since 45-nm
  But … logic density has been ~doubling and power/performance increasing by 15% per node
  N3E/N5 Density = 1.5X (typical chip)
Source: Techsearch, AMD
Source: Datacore
Amdahl’s Law (1967)
  Increasing system performance by parallelizing CPUs and multi-threading
  But … I/O Speed hasn’t been keeping up with CPU parallelization causing system bottlenecks (I/O speeds double every 4 years)

## Slide 6: Faster Evolution of Protocols
Chart: 
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
PCIe | 8 | 16 | 32 | 64 | 128 | 256 | 512
Bandwidth
Chart: 
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
HBM | 128 | 256 | 307 | 410 | 461 | 819 | 1075
HBM | 128 | 256 | 307 | 410 | 461 | 819 | 1075
Chart: 
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
USB | 0.48 | 5 | 10 | 20 | 40 | 80
Chart: 
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
 | 2.4 | 8.5 | 17 | 26 | 35.2 | 51 | 67 | 70 | 140 | 200
Bandwidth
Bandwidth
Bandwidth
Protocol Evolution
Standards accelerating to address IO bandwidth gap
Historically ~ 4 yrs between revisions, but accelerating ~2 yrs
Each requires a new PHY architecture + multiple ports + customizations
Synopsys has the experience and scale to reduce risk and meet aggressive TTM

## Slide 7
“Day of Reckoning”
Predicted by Gordon Moore
“ It may prove to be more economical to build large systems out of smaller functions, which are separately packaged and interconnected.”
Courtesy Intel
Source: https://newsroom.intel.com/wp-content/uploads/sites/11/2018/05/ moores-law-electronics.pdf
Animation 1
Animation 2
Animation 3
Animation 4
Animation 5
Animation 6
Animation 7
Animation 8
Animation 9
Animation 10
Animation 11
Animation 12

## Slide 8: Multi-Die Systems Accelerating Now
Design Starts Growing 5X in 5 Years
Source: IP Nest 2022
Chart: 
| 2021 | 2022 | 2023 | 2024 | 2025 | 2026
 | 30 | 48 | 68 | 104 | 124 | 150
Enabling new levels of functionality and integration for advanced systems
Innovations in packaging drives capabilities
Adopted by multiple market segments today
Significant new challenges for silicon designers abound
Multi-Die System Design Starts

## Slide 9: Real World Examples of Multi-Die Systems
Scale & Disaggregate IO
  16 Compute Die +
  8 Cache Die + 2 Base Die
  8 HBM Die + 2 IO Die
EMIB + Foveros Pkg
Scale use case
  2 Compute Die
Silicon Interposer Pkg
Disaggregate IO
  1 Compute Die +
  4 DDR Die + 2 I/O Die
Substrate Pkg
Scale & Disaggregate IO
  8 Compute Die +
  1 I/O Die
Substrate Pkg
Apple
M1 UltraMax CPU
Intel
Ponte Vecchio Xe-HPC GPU
AMD
EPYC Server CPU
Amazon
Graviton3 Server CPU

## Slide 10: AMD EPYC
8 Compute Dies in 7nm, 1 IO Die in 14nm on Organic Substrate
Proprietary D2D Link – Infiniti Fabric
Resulted in significant lower cost vs. monolithic die Enabled multiple SKUs for a series of Processors (different CPU / DRAM configurations)

## Slide 11: Lower System Cost
Smaller Die with Improved Yield Offsets Higher Silicon Area and Package/Test Cost
Hypothetical monolithic 32-core chip compared to an assembly of four eight-core chiplets
772mm2 versus 852mm2 (+9.7%)
Relative cost = 0.59X
Pioneering Chiplet Technology and Design for the
AMD EPYC™ and Ryzen™ Processor Families
AMD 2021 ACM/IEEE 48th Annual International Symposium on Computer Architecture (ISCA)
Multi-die systems will become more attractive as advanced packaging volumes increase & costs decline
Monolithic SoC
I/O
Memory
CPU Core
Memory
Memory
Memory
I/F
I/F
CPU Core
I/O
I/F
I/F
Memory
Memory
Memory
Memory
CPU Core
Memory
Memory
I/O
I/O
CPU Core
Multi-Die System
I/F
I/F
I/F
I/F
CPU Core
Memory
Memory
I/O
I/O
CPU Core
I/F
I/F
I/F
I/F
CPU Core
Memory
Memory
I/O
I/O
CPU Core
I/F
I/F
I/F
I/F
CPU Core
Memory
Memory
I/O
I/O
CPU Core
I/F
I/F
I/F
I/F

## Slide 12: Apple M1 Ultra
2 Compute Dies in 5nm, 8 LPDDR5 Die in an InFO-L Package
Proprietary D2D Link – Ultra Fusion
Power/area efficient Scaling (57B Transistors, 10 CPUs, 64 GPUs) with 2.5TB D2D Bandwidth
Created multiple SKUs – 1 Die for Laptop, 2 Dice for Desktop

## Slide 13: Common Commercial Use Cases
Disaggregating IOs
Aggregating Functions
Scaling Processing SoCs
Splitting SoCs
Homogenous Die
Heterogeneous Die
Multiple, scalable clusters of CPUs
Scalable systems, multiple SKUs
Ideal D2D link looks like wire
5-nm  3-nm
CPU, Accelerators
Aggregate multiple disparate functions
Reduce cost/form Factor
5G Base Station, Co-Packaged Optics
Large compute & switch dies approaching reticle limit
All about cost/yield (30% less)
Ideal D2D link looks like wire
5-nm  3-nm
Accelerators, Switch
Split Servers: Processing & I/O Chips
Processor chases Moore’s Law
I/O chip in N-2
Risk, cost, reuse, TTM
CPU, FPGA & Switch

## Slide 14: The Drive to Multi-Die Systems
Motivation for Multi-Die Systems
Accelerated scaling of system functionality at a cost-effective price (>2X reticle limits)
Reduced risk & time-to-market by re-using proven designs/die
Lower system power while increasing throughput (up to 30%)
Rapid creation of new product variants for flexible portfolio management

## Slide 15: Multi-Die Now, Tracking 100 Design Starts
By Application
Customers Don’t Want to Go There … But They Have to go There in Some Applications
Chart: 
| Server/AI | Edge Server/AI | Networking | Auto | Industrial | Consumer | Storage | Other
 | 43 | 6 | 13 | 13 | 5 | 3 | 5 | 10

## Slide 16: But it’s Not That Easy! Multi-Die System Challenges
Transformation from Monolithic SoC to Multi-Die Systems
Heterogeneous system integration
Die-to-die connectivity
Power & thermal management
Software development & modeling
Capacity/performance for system verification
System pathfinding
System signoff analysis
System yield
Hierarchical Test & Repair
Memory utilization & coherency
Reliability & Security
Challenges
Multi-Die
Systems
Monolithic
SoC
GPU
CPU
Memory
IO

## Slide 17: But it’s Not That Easy! Multi-Die System Challenges
Transformation from Monolithic SoC to Multi-Die Systems
Heterogeneous system integration
Die-to-die connectivity
Power & thermal management
Software development & modeling
Capacity/performance for system verification
System pathfinding
System signoff analysis
System yield
Hierarchical Test & Repair
Memory utilization & coherency
Reliability & Security
Challenges
Multi-Die
Systems
Monolithic
SoC
GPU
CPU
Memory
IO

## Slide 18: 4 Alliances & 5 Standards Across Ecosystem
Technical Merits, Maturity & Strength of Ecosystem are Key for Success
Alliance |  |  |  |  | 
Standard | XSR | BOW | OHBI | AIB | UCIe
Data Rate | 112G / 224G | 8G / 16G | 8G / 16G | 6G | 16G / 32G
Protocol | Not Defined | Not Defined | Not Defined | Not Defined | Streaming, PCIe, CXL
Package Focus | 2D | 2D (2.5D also supported) | 2.5D (2D also supported) | 2.5D | 2D, 2.5D
Target Applications | Optical Networking (CPO/NPO) | Cost sensitive aggregation | High density scale for data center | Mil-aero ecosystem | Scale & Split w/ streaming Aggregation w/ PCIe/CXL

## Slide 19: Summary of 5 Main D2D Standards
Key Figures of Merit: Technical (Bandwidth, Power, Latency) & Cost
0.2
1.6
0.4
0.6
1.2
1.4
0.8
1.0
500
9500
8500
7500
6500
5500
1500
2500
3500
4500
1000
2000
3000
4000
5000
6000
7000
8000
9000
10000
LOW Bandwidth per Edge Width (Gbps/mm) HIGH
HIGH Power (pJ/bit) LOW
OHBI 32G
OHBI 16G
OHBI 24G
OHBI 8G
XSR 112G
XSR 224G
UCIe 8G
UCIe 16G
UCIe 32G
UCIe 32G
UCIe 16G
AIB 2G
AIB 6G
BOW 16G
BOW 8G
Conclusions Based on Metrics
UCIe offers better metrics at same data rate
Latency similar across OHBI/UCIe, lower than XSR
UCIe 16G PHYs serve HPC for next 3 years
UCIe 32G PHYs for high end AI and next generation networking needed starting in ~2025
Interposer
$$$
Organic
Substrate
$

## Slide 20: 4 Alliances & 5 3 Standards Across Ecosystem
Technical Merits, Maturity & Strength of Ecosystem are Key for Success
Alliance |  |  |  |  | 
Standard | XSR | BOW | OHBI | AIB | UCIe
Data Rate | 112G / 224G | 8G / 16G | 8G / 16G | 6G | 16G / 32G
Protocol | Not Defined | Not Defined | Not Defined | Not Defined | Streaming, PCIe, CXL
Package Focus | 2D | 2D (2.5D also supported) | 2.5D (2D also supported) | 2.5D | 2D, 2.5D
Target Applications | Optical Networking (CPO/NPO) | Cost sensitive aggregation | High density scale for data center | Mil-aero ecosystem | Scale & Split w/ streaming Aggregation w/ PCIe/CXL

## Slide 21: UCIe is the Preferred D2D Interface!
Technical Merits, Comprehensive Spec & Broad Eco-System
Technical Merits (Most compelling PPAs)
  Energy efficiency <0.3pJ/Bit
  Edge efficiency >5Tbps/mm
  Latency ~2ns from Pin to FDI
Comprehensive & Futureproof
  All use cases
  All package types
  Chip to Chip use case with retimer
  Complete protocol stack
  Future proof with support up to 32Gbps data rate per pin
Broad Eco-System
  Wide range of promoters & contributors spanning all industry segments
> 100 members (Dec.2022)

## Slide 22: What Standard Do You Plan to Use for D2D Interface?
"Don't know" responses are excluded from analysis.
GLOBAL 2022
Chart: 
| Other | BOW | OpenHBI | USR/XSR | UCIe | Proprietary
2022 | 0.0238 | 0.1143 | 0.1571 | 0.2524 | 0.3143 | 0.3429
2022 N = 210
No historical data as these are new questions starting 2022.
Percentages equal >100% because multiple answers were accepted.
  "Source: Synopsys Global User Survey YEAR(S) – used with Synopsys’ permission."

## Slide 23: UCIe Built to Enable Common and New Use Models
UCIe Is Highly Flexible
Server or AI Scaling (Homogeneous)
(NoC-to-NoC with low latency & coherency)
UCIe Streaming
CXS or AXI bridge
User Defined / Proprietary
Server
Server
Heterogeneous Computing (Accelerator)
(Interoperability with low latency & coherency)
UCIe CXL or PCIe
For interoperability
UCIe Streaming
CXS or AXI bridge
Server
Accelerator
Resource Aggregation (Pooling) w/Retimer
(Rack-to-Rack with low latency)
UCIe CXL or PCIe6
For Aggregation
UCIe Streaming
For CPO / Eth.
Server
Accelerator
SiPh
SiPh
IO or Memory Split
(Interoperability with low latency)
UCIe CXL or PCIe6
Coherency for Memory
UCIe Streaming
AXI bridge for Ethernet
Server
Memory
Ethernet

## Slide 24: IP Must Support Multiple Package Types
Considerations: Power, Performance, Area, Latency & Cost Trade-Offs
By Package
Chart: 
| CoWoS | CoWoS-S | EMIB | FOCoS-CL | InFO | CoWoS | Substrate | 3D | Adv | Std | 3D
Total | 11 | 7 | 17 | 1 | 3 | 1 | 52 | 1

## Slide 25: 2.5D Packaging Technologies Evolving for Higher Integration
Summary of Relative Cost & Density Attributes
DENSITY
COST
Organic Substrate
Cost: 0.2–0.4x
Pitch: 90mm–110mm
IO/mm2: 83–123
Laminate w/Si Bridge
Cost: 0.4x
Pitch: 55mm
IO/mm2: 331
Interposer
Cost: 1.0x
Pitch: <40mm
IO/mm2: 625
Source: Jan Vardaman, Tech Search Inc.
Fan-out w/Si Bridge
Cost: 0.6x
Pitch: 25mm
IO/mm2: 350
Fan-out (RDL)
Cost: 0.5x
Pitch: 40mm
IO/mm2: 330
High Density Org Sub
Cost: 0.3 to 0.4x
Pitch: 55mm
IO/mm2: 331
Die 1
Die 2
Die 1
Die 2
Die 1
Die 2
Die 1
Die 2
Die 1
Die 2
Die 1
Die 2
Die 3

## Slide 26: Magic Decoder Ring - 2.5D & 3D Technology Names
 | Technology | TSMC | Samsung | Intel | ASE
2.5D | RDL Fan Out | TSMC InFO-oS/ TSMC InFo-PoP |  |  | ASE FOCoS-CF
 | Bridge | CoWoS_L |  | EMIB | FOCoS-B
 | Interposer | CoWoS_S CoWoS_R | ICUBE H-CUBE R-CUBE |  | FOCoS-CL
3D | Hybrid Bonding | SoIC | X-Cube | Foveros Omni Foveros Direct | 
Leading Manufacturers: TSMC, Samsung, Intel & ASE

## Slide 27: IP Required By Package & Across Nodes
Need To Support Multiple Technology Nodes Across Multiple Foundries & Packages
By Node
By Package
Chart: 
| CoWoS | CoWoS-S | EMIB | FOCoS-CL | InFO | CoWoS | Substrate | 3D | Adv | Std | 3D
Total | 11 | 7 | 17 | 1 | 3 | 1 | 52 | 1
Chart: 
| 3 | 5 | 7 | 12 | 28+
 | 23 | 36 | 14 | 16 | 4

## Slide 28: Synopsys UCIe IP Leverages Generations of D2D & HBM IP
Track Record with Multi-Die System PHY Products
HBI 2Gbps Sams 14nm 2.5D (I)
HBI+ 4Gbps TSMC 7nm
2.5D (I+B)
HBI+ 4Gbps TSMC 5nm
2.5D (I)
HBI+ 4Gbps GF 12nm 2.5D (I)
OpenHBI 16Gbps TSMC 3nm 2.5D (I)
AIB2.0 4Gbps Intel 16nm
2.5D (B)
UCIe 16Gbps TSMC 3/5/7nm 2.5D (I+B) 2D (S)
HBM2e 3.6Gbps TSMC 7nm 2.5D (B)
HBM3 9.6Gbps TSMC 3nm 2.5D (I)
Several Products, TSMC 7nm, 6nm, 5nm
90% complete
Not Taped-out
Prioritize UCIe
D2D (AIB/HBI & XSR) and HBM IP in production with several customers using Interposer and Bridge packaging
Package type: 2.5D: I – Interposer, B – Bridge / 2D: S – Substrate
XSR 112Gbps TSMC 7nm 2D (S+I)
XSR 112Gbps TSMC 12nm 2D (S)
XSR 112Gbps GF 12nm 2D (S)
XSR 112Gbps TSMC 6nm 2D (S)
XSR 112Gbps TSMC 5nm 2D (S)
Production
Production
Production
Production
Production
Production
Tapeout
In Lab
Silicon Proof
Silicon Proof
HBM3 7.2Gbps TSMC 5nm 2.5D (I)
Tapeout
HBM3 6.4Gbps TSMC 6nm 2.5D (I)
Production
Extensive Packaging Expertise

## Slide 29: Robust and Secure IP for Multi-Die Systems
UCIe Verification IP
Scalable architecture to support verification of various DUT types
Build-in protocol checks and functional coverages at all layers
UCIe PHY IP
Low latency & power for interposer & substrate designs
Extensive test & debug features for KGD
UCIe Controller IP
Low latency bridge for NoCs in a multi-die system
Optional security engine with encryption
Synopsys UCIe Die-to-Die IP: Complete Solution Based on Silicon-Proven Technology
Multi-Die System
PHY
Advanced/Standard Packages
Controller
Interface Bridge (CXS/AXI)
Protocol Layer (CXL/PCIe)
D2D Adapter
Security
Verification IP
SiPi
Subsystems
Test & Diagnostics

## Slide 30: Synopsys UCIe Solution Summary
Wide Process Coverage to Enable Expanding Multi-Die System Ecosystem
 In Planning
Process Node | UCIe PHY | 
 | UCIe-A | UCIe-S
TSMC N3P | n | n
TSMC N3E | n | n
TSMC N4P | n | n
TSMC N5 | n | n
TSMC N6/7 | n | n
TSMC 12/16FFC |  | n
Samsung 3GAP | n | n
Samsung 4LPP | n | n
Samsung 5LPe | n | n
Intel | n | n
Global Foundries | n | n
 Committed Timelines
UCIe-A = Advanced Packaging
UCIe-S = Standard Packaging
UCIe Controller |  |  |  | 
Base (Stream) | CXS.B Bridge | AXI Bridge | CXL | PCIe
n | n | n | n | n
Contact Synopsys for existing XSR IP Solution, Controller & PHY, Availability

## Slide 31: Expanded Design Support for UCIe
With Synopsys 3DIC Compiler and Package / SIPI Analysis
Advanced Package Design
3DIC Compiler Reference designs, training & application notes
UCIe-Route – Auto-routing & PPA intelligence built into Synopsys’ 3DIC Compiler
SI PI Analysis
Insertion Loss [dB]
Return Loss [dB]
Escape studies, Std. & Adv. Packages
Floorplan analysis for UCIe multi-module configs
Package characteristics alignment with UCIe variants
CoWoS Pattern Study
Substrate Escape Study

## Slide 32: Synopsys IP Chiplets for Multi-Die Systems
SYNOPSYS IP CHIPLETS
Built on Synopsys’ silicon-proven, high-quality IP portfolio
Flexibility to support multiple package types
Customizable to target application
Key features
  Standards-compliant Die-to-Die interfaces
  Hierarchical test
  Built-in security
  Silicon lifecycle management
  Yield enhancement functionality to save system cost
Integrated & ready for tapeout for fast time-to-market
BROAD IP PORTFOLIO
Silicon proven
High quality
Secure
Interface IP
Processor IP
Foundation IP
Security IP
IP SUBSYSTEMS
Configured Interfaces (ie, PCIe Subsystem)
Pre-validated
Integration-ready
IP CHIPLETS
…
Ethernet IO Chiplet
Memory Expander Chiplet
AI Accelerator Chiplet

## Slide 33: Synopsys IP Portfolio
Digital IP
AMBA 4 AXI, AMBA 3 AXI & AMBA 2.0 AHB
Die-to-Die
controller
DDR/HBM controller
USB controller
PCIe controller
HDMI/DP controller
Ethernet
controller
CSI
DSI
Safety Security
UFS
UniPro
Datapath, incl. Floating Point Elements
SD/eMMC controller
BLE 5 Link Layer
Physical IP
UCIe/XSR
PHY
DDR/HBM PHY
USB PHY
PCIe PHY
HDMI/DP
PHY
10/56/112G
PHY
C/D-PHY
M-PHY
Logic Libraries
ADCs
DACs
Embedded Memories
(TCAM, SRAM, ROM, NVM)
eMMC PHY
PVT Sensors
GPIOs, LVDS
BLE Radio
ARC Processor IP
CPUs MPUs
DSPs
IP Subystems
AI & ML
Processor
SYNOPSYS IP PORTFOLIO
Software
Broadest Portfolio
Foundation IP, Analog, Interfaces, Security,
Processors, Subsystems
Highly Differentiated
Delivering IP at the Cutting Edge of Technology & Functionality Across Key Markets
Committed to Your Success
5,800+ IP Engineers Worldwide Dedicated to Quality

## Slide 34: Synopsys Multi-Die System Solutions
Manufacturing
& Reliability
Architectural Exploration
Design Implementation
Software Dev. & Validation
A Comprehensive Solution for Heterogeneous Integration
Optimize thermal, power, and performance with early exploration and partitioning
Rapid software development and validation with high-capacity emulation & prototyping
Efficient die/package co-design with unified exploration-to-signoff platform and robust IP
Improve health, security and reliability with holistic test and lifecycle management solutions
IP Chiplets
SW Dev. & System Validation
System Signoff
Verification
Test & Repair
Silicon IP
Silicon Lifecycle Management
Thermal/ Power Analysis
Architectural Exploration
Multi-Die/Package Co-Design

## Slide 35: Multi-Die Systems: The Next Wave of System Design
Initial markets: HPC/Server, AI accelerators, automotive, and mobile--and expanding
Significant system benefits
  Reduced cost, increased functionality, reduced schedules, increased flexibility
Significant challenges to navigate
  Security, standard interfaces, power and thermal management, predictive analysis for reliability
Synopsys is your preferred EDA and IP partner for multi-die systems
  Architectural exploration to optimize thermal, power, performance
  Software development and system validation
  Design implementation from exploration to signoff
  Robust & secure die-to-die IP
  Manufacturing & reliability with hierarchical test, diagnostics and repair
  Silicon Lifecycle Management from die to fleet of multi-die systems
Synopsys is Your Partner for Successful Multi-Die Systems